Machining with a Lathe

---
Machining with a Lathe

---
Machining with a Lathe

---
Mori Seiki DuraTurn CNC Lathe

---
Lathe Coordinate System

---
Workpiece Zero Point
Coordinate system zero point is
  - centerline of spindle (X zero)‏
    - with normal spindle rotation, machining is in +X
  - back face of part (Z zero)
    - +Z is machining part
X dimensions are diameter, not radius

---
Workpiece Zero Point

---
Workpiece Zero Point
+
X=0
-
Stock is 50 + 10mm
by 38.1mm diam.
- Z=0 +

---
Lathe Tooling
- Turning
- Boring
- OD Grooving
- ID Grooving
- Face Grooving
- OD Threading
- ID Threading

---
Z=0

---
Absolute Programming
- Point 1 :	X40.0	Z90.0
- Point 2:	X50.0	Z85.0
- Point 3:	X50.0	Z40.0
- Point 4:	X80.0	Z40.0
- Point 5:	X100.0	Z30.0

---
Incremental Programming
- In incremental programming, only the change in X and Z are given. Change in X is U, change in Z is W.
- ONLY USE FOR MOVING AWAY FROM PART, NOT CUTTING!
- Point 1:	X40.0	Z90.0
- Point 2:	U10.0	W-5.0
- Point 3: W-45.0
- Point 4:	U30.0
- Point 5:	U20.0	W-10.0

---
CNC Lathe Programming

---
G-Codes for Turning
Limit spindle speed
G50
Return to reference point
G28
Metric system
G21
Inch system
G20
Dwell
G4
CCW Circular interpolation
G3
CW Circular interpolation
G2
Linear interpolation (feeding)‏
G1
Rapid positioning
G0

---
G-Codes for Turning
Feed per revolution mode
G99
Feed per minute mode
G98
Constant spindle speed mode
G97
Constant surface speed mode
G96
Threading cycle
G76
Facing cycle
G72
Roughing cycle
G71
Finishing cycle
G70
Select work coord system #1
G54

---
M-Codes for Turning
Program end
M30
Open chuck
M11
Close chuck
M10
Stop coolant
M9
Start coolant
M8
Stop spindle
M5
Start spindle (reverse rotation)‏
M4
Start spindle (normal rotation)‏
M3
Optional Program Stop
M1
Program Stop
M0

---
Variables and Math
Variables:
  - #1-33 (local vars for macros)
  - #100-199 (zeroed on powercycle)
  - #500 to 999 (survive powercycle)
  - Don't change vars above #1000: these are system variables.
  - math:
    - [#500 + 1.0]
    - [#500 + #510]
    - [#500 + [#512/2.0]]

---
Example Program
%
O1 (THAT'S AN OH NOT A ZERO)
; (EXAMPLE PROG - TURN PLUG 20.0MM OD X 17MM LONG)
; (STOCK: ALUM 1.5" X 17MM + 10MM)
; (T1- CNMG 55DEG DIAMOND)
; (T2- VNMG 15DEG DIAMOND)
; (T10- 3.175MM CUTOFF)
;
; (VARIABLES)
#500=38.1 (STOCK DIAMETER)
#501=17.0 (STOCK LENGTH)
#502=300.0 (SURFACE M/MIN FOR CUTTING ALUM)
#503=0.2 (ROUGHING FEED- MM/REV)
#504=0.02	(FINISH FEED- MM/REV)
;
N1
G54 (WORK OFFSET)
G21 (METRIC)
G28 U0 W0 (GO HOME)
G50 S2000 (MAX SPINDLE SPEED)

---
; (ROUGH OD 38.0 TO 20.5MM)
; (USE 2.0MM DEPTH OF CUT -> 8 PASSES)
;
N2
G00 T0101 (55DEG DIAMOND TOOL, TOOL 1)
G50 S2000 (CLAMP SPEED AT MAX 2000)
G96 S#502 (CONST SURF SPEED)
G99 (FEED PER REV)
G00 X[#500 + 0.5] Z#501 (INITIAL POINT FOR ROUGHING)
M03 (SPINDLE ON)
M08 (TURN ON COOLANT)
G00 X36.0 Z#501
G01 X36.0 Z5.5 F#503 (FIRST PASS)
G01 X[#500+0.5] F#503 (RETRACT X)
G00 Z#501 (RETRACT Z)
G00 X34.0
G01 X34.0 Z5.5 F#503 (SECOND PASS)
G01 X[#500+0.5] F#503
G00 Z#501
G00 X32.0
G01 X32.0 Z5.5 F#503 (THIRD PASS)
G01 X[#500+0.5] F#503
...

---
;
; (FINISH OD 20.0MM)
;
N3
G00 T0202 (VNMG 15DEG DIAMOND)
G00 X19.0 (POSITION FOR START OF CHAMFER)
G00 Z[#501+0.5]
G01 X20.0 Z[#501-0.5] F#504 (CHAMFER 0.5MM)
G01 Z0.0 F#504 (FINISH TURN)
G01 X[#500+0.5] F0.1 (BACK OFF)
M09
M05
G28 U0 W0 (GO HOME)
M01

---
;
; (CUTOFF)
G00 T1010
G00 Z0.0 (CUTOFF BLADE TOOLPOINT IS ON RIGHT SIDE)
G00 X[#500+2.0]
M03
M08
G50 S1000 (CLAMP SPEED AT MAX 1000RPM)
G96 S#502 (CSS)
G01 X-0.5 F0.05 (CUTOFF)
G01 X[#500+2.0] F4.0 (RETRACT)
M09
M05
G28 U0 W0
M30 (END PROGRAM)
%

---
Special Tips
- NEVER DO A TOOL CHANGE AWAY FROM HOME! (G28 U0 W0)‏
- ALWAYS PUT A DECIMAL POINT AFTER DIMENSIONAL NUMBERS (no decimal --> microns)‏
- USE ALL CAPS IN YOUR PROGRAM (lowercase gets dropped)‏
- DON'T GET “OHS” AND “ZEROS” MIXED UP. PROGRAM NAME STARTS WITH “OH”, NOT ZERO