Discrete Position Sensing
- Mechanical
- Optical
- Magnetic

---
Mechanical Sensing - Microswitch

---
Microswitch Operation
Switch exhibits mechanical hysteresis.

---
Microswitch Actuators

---
Optical Sensing
- LED’s and Photodiodes
- Transmissive/Reflective
- Modulated/Unmodulated
- Light-on/Dark-on
- Fiber optic

---
Transmissive & Reflective Sensors

---
Beam Pattern and Reflectance

---
Specular Reflection

---
Modulation
- “Chop” LED on and off at many kHz rate
- Bandpass filter after photodiode at the same frequency as chopping
- Threshold circuit after BPF generates on/off output

---
Magnetic Position Sensors
- Inductive proximity sensors (eddy current, sense metal)
- Reed switches (sense permanent magnet)
- Hall Sensors (sense permanent magnet)

---
Inductive Proximity Sensor

---
Inductive Proximity Sensors

---
Hall Sensors
Hall effect:
  - constant voltage forces a constant current in semiconductor sheet
  - magnetic field flux lines perpendicular to current cause proportional voltage across sheet.
  - discovered by E.F.Hall in 1879
- Linear sensor needs voltage regulator and amplifier
- Switch also needs threshold circuit, with hysteresis

---
Hall Switch
Magnet motion
  - head-on
  - bypass or slide-by
- Total effective air gap
- Sensitivity, Hysteresis, & Temperature

---
Sinking/Sourcing
The tag indicates that the LOAD (PLC input) has a +DC common
  - this is a sinking output
  - Sinking output => sourcing input

---
Sinking/Sourcing, NC/NO
1. How do you choose sensor logic?
2. - think about failure modes
3. - if tripped = stop moving and short to ground more likely than short to +v, use NC and sourcing
4. (broken wire = tripped, short to gnd = tripped)

---
Sinking/Sourcing
Photosensor – comes in either NPN (sinking) or PNP (sourcing)

---
Terminal Blocks