Making Parts
1. Machining (subtractive manufacturing)
2. 3D Printing (additive manufacturing)

---
3D Printing
- + Complex geometries
- + No tooling
- - Anisotropic material properties
- - Porosity
- - Post-processing
- +/- Cost
- +/- Print time

---
Slicing

---
Fillets

---
Overhangs

---
Supports

---
Holes

---
Fastening
1. - Tapped holes (for very light loads)
2. - nut pockets
3. - heat set inserts
4. - adhesives (CA for PLA)

---
Creality Ender 3 S1
1. 0.4mm nozzle
2. Usually 0.2mm layers (slicer setting dependent)
3. 20% infill default slicer setting

---
Stratasys Eden 500V Polyjet
1. - “Inkjet” printing of UV cured resin
2. - 600dpi resolution (42um)
3. - 16um layer thickness
4. - 500x400x200mm build volume
5. - parts are fully dense, almost isotropic
  - printing is done in 50mm wide passes
6. - all overhangs receive printed support
https://photos.google.com/photo/AF1QipNliV-IHkC_1cU3RbFWLXUYGq6ti4Rh8PClPCSs

---
Comparison

---
Comparison
1. Creality Ender 3 S1, Cura slicer
2. 20% infill:	8g/0g	1:04	$ 0.13
3. 100% infill: 12g/0g	1:26	$ 0.19
5. Eden 500V, Stratasys/Objet slicer
6. 100%, 1x:	18g/11g	0:20	$ 4.60
7. 100%, 4x:	68g/37g	0:24	$16.93

---
Eden 500V

---
Eden 500V

---
MH5L Robot

---
MH5L Specs

---
Work Envelope

---
MH5L Wrist Flange

---
MH5L Internals

---
Robot Coordinate Systems
- Joint Coordinates
1. - Base Coordinates

---
Robot Coordinate Systems
- Tool Coordinates
- Custom Coordinates