Z=0

---
Absolute Programming
- Point 1 :	X40.0	Z90.0
- Point 2:	X50.0	Z85.0
- Point 3:	X50.0	Z40.0
- Point 4:	X80.0	Z40.0
- Point 5:	X100.0	Z30.0

---
CNC Lathe Programming

---
G-Codes for Turning
Limit spindle speed
G50
Return to reference point
G28
Metric system
G21
Inch system
G20
Dwell
G4
CCW Circular interpolation
G3
CW Circular interpolation
G2
Linear interpolation (feeding)‏
G1
Rapid positioning
G0

---
G-Codes for Turning
Feed per revolution mode
G99
Feed per minute mode
G98
Constant spindle speed mode
G97
Constant surface speed mode
G96
Threading cycle
G76
Facing cycle
G72
Roughing cycle
G71
Finishing cycle
G70
Select work coord system #1
G54

---
M-Codes for Turning
Program end
M30
Open chuck
M11
Close chuck
M10
Stop coolant
M9
Start coolant
M8
Stop spindle
M5
Start spindle (reverse rotation)‏
M4
Start spindle (normal rotation)‏
M3
Optional Program Stop
M1
Program Stop
M0

---
Incremental Programming
- In incremental programming, only the change in X and Z are given. Change in X is U, change in Z is W.
- ONLY USE FOR MOVING AWAY FROM PART, NOT CUTTING!
- Point 1:	X40.0	Z90.0
- Point 2:	U10.0	W-5.0
- Point 3: W-45.0
- Point 4:	U30.0
- Point 5:	U20.0	W-10.0

---
Variables and Math
Variables:
  - #1-33 (local vars for macros)
  - #100-199 (zeroed on powercycle)
  - #500 to 999 (survive powercycle)
  - Don't change vars above #1000: these are system variables.
  - math:
    - [#500 + 1.0]
    - [#500 + #510]
    - [#500 + [#512/2.0]]

---
Example Program
%
O1 (THAT'S AN OH NOT A ZERO)
; (EXAMPLE PROG - TURN PLUG 20.0MM OD X 17MM LONG)
; (STOCK: ALUM 1.5" X 17MM + 10MM)
; (T1- CNMG 80DEG DIAMOND)
; (T10- 3.175MM CUTOFF)
;
; (VARIABLES)
#500=38.1 (STOCK DIAMETER)
#501=17.0 (STOCK LENGTH)
#502=300.0 (SURFACE M/MIN FOR CUTTING ALUM)
#503=0.2 (ROUGHING FEED- MM/REV)
#504=0.02	(FINISH FEED- MM/REV)
;
N1
G54 (WORK OFFSET)
G21 (METRIC)
G28 U0 W0 (GO HOME)
G50 S2000 (MAX SPINDLE SPEED)

---
; (ROUGH OD 38.0 TO 20.5MM)
; (USE 2.0MM DEPTH OF CUT -> 8 PASSES)
;
N2
G0 T0101 (80DEG DIAMOND TOOL, TOOL 1)
G50 S2000 (CLAMP SPEED AT MAX 2000)
G96 S#502 (CONST SURF SPEED)
G99 (FEED PER REV)
G0 X[#500 + 0.5] Z#501 (INITIAL POINT FOR ROUGHING)
M3 (SPINDLE ON)
M8 (TURN ON COOLANT)
G0 X36.0 Z#501
G1 X36.0 Z5.5 F#503 (FIRST PASS)
G1 X[#500+0.5] F#503 (RETRACT X)
G0 Z#501 (RETRACT Z)
G0 X34.0
G1 X34.0 Z5.5 F#503 (SECOND PASS)
G1 X[#500+0.5] F#503
G0 Z#501
G0 X32.0
G1 X32.0 Z5.5 F#503 (THIRD PASS)
G1 X[#500+0.5] F#503
...

---
;
; (FINISH OD 20.0MM)
;
N3
G0 T0101
G0 X19.0 (POSITION FOR START OF CHAMFER)
G0 Z[#501+0.5]
G1 X20.0 Z[#501-0.5] F#504 (CHAMFER 0.5MM)
G1 Z0.0 F#504 (FINISH TURN)
G1 X[#500+0.5] F0.1 (BACK OFF)
M9
M5
G28 U0 W0 (GO HOME)
M1

---
;
; (CUTOFF)
G0 T1010
G0 Z0.0 (CUTOFF BLADE TOOLPOINT IS ON RIGHT SIDE)
G0 X[#500+2.0]
M3
M8
G50 S1000 (CLAMP SPEED AT MAX 1000RPM)
G96 S#502 (CSS)
G1 X-0.5 F0.05 (CUTOFF)
G1 X[#500+2.0] F4.0 (RETRACT)
M9
M5
G28 U0 W0
M30 (END PROGRAM)
%

---
Special Tips
- NEVER DO A TOOL CHANGE AWAY FROM HOME! (G28 U0 W0)‏
- ALWAYS PUT A DECIMAL POINT AFTER DIMENSIONAL NUMBERS (no decimal --> microns)‏
- USE ALL CAPS IN YOUR PROGRAM (lowercase gets dropped)‏
- DON'T GET “OHS” AND “ZEROS” MIXED UP. PROGRAM NAME STARTS WITH “OH”, NOT ZERO

---
Planning a Program
Critical dimensions
  - if your most critical dimension is an OD, do OD turning first
  - if your most critical dimension is an ID, do boring first
Machining ID
Drill, rough bore (with end mill), finish bore (with boring bar)
be very careful retracting from ID operations. It is too easy to crash a tool inside the part and break the tool. ID tools are much more expensive as well as much more fragile than OD tools.

---
Planning a Program
Finish passes
  - if your tolerance is tight or your part is slender (so it may deflect noticeably), run multiple finish passes at the same diameter.

---
G-Code Looping & Branching
Loops:
  - WHILE [#500 GT #510] DO 1
    - G01 ...
    - #500 = #500 – 0.2
  - END 1
Conditionals:
  - IF [#502 LE #515] GOTO N100
  - ...
  - N100

---
ROUGHING CYCLE - G71

---
Roughing Cycle - G72

---
Finishing Cycle - G70

---
G71/G70 Cycle (OD example)
M09
M05
G28 U0 W0
G0 T0202
G50 S4000
G96 S#502
G99
G0 X[#500 + 10.0] Z[#501 + 10.0] (CLOSE)
M3
G0 X#500 Z[#501 + 2.5] (INITIAL POINT)
M8
G70 P100 Q110 (EXACT PROFILE FOR FINISH)
M9
M5
G28 U0 W0
G0 T0101
G50 S2000
G96 S#502
G99
G0 X[#500 + 10.0] Z[#501 + 10.0] (CLOSE)
M3
G0 X#500 Z[#501 + 2.0] (INITIAL POINT)
M8
G71 U2.0 R0.75 (2MM DOC, 0.75MM RET)
G71 P100 Q110 U0.5 W0.25 F#503 (LEAVE 0.5MM ON OD 0.25MM ON FACES)
N100 G0 X0.0 Z[#501 + 2.0] (START POINT)
G1 Z#501 F#504
X10.0
Z7.0
X14.0 Z5.0
Z-3.2
N110 G0 X[#500 + 2.0] (EXIT)

---
Arcs
G2 = CW arc
G3 = CCW arc
Parameters:
  X,Z = end point of arc
  I,K = distance to center point of arc from start
  (I is in radius units, not diameter units)
  F = feedrate

---
Convex Arc Example
G0 X0.0 Z19.0 (START POINT)
G3 X38.0 Z0.0 I0.0 K-19.0 F0.1 (CCW)

---
Convex Arc Example
G71 U2.0 R0.75 (2MM DOC, 0.75MM RETRACT)
G71 P100 Q110 U0.5 W0.25 F#503
N100 G00 X0.0 Z19.0 (ENTRANCE POINT)
G03 X38.0 Z0.0 I0.0 K-19.0 F#504
G01 X38.0 Z-3.2
N110 G00 X[#500+2.0] (EXIT)
G70 P100 Q110 F#504 (FINISH PASS)

---
Concave Arc Example
- Drill center hole
- Use boring tool to rough and finish cavity
G0 X0.0 Z15.0
G2 X30.0 Z10.0 I0.0 K25.0 F0.2

---
Threading Cycle
- Threading requires multiple passes in perfect synchronization to reach final thread depth.
- Must make sure you are in constant spindle speed mode, not constant surface speed!

---
Computing Thread Parameters
Overall thread height
  - H = Pitch*(0.5 / tan 30deg) = 0.866025*Pitch
  - Ext thread depth = (17/24)*H = 0.613435*Pitch
  - Int thread depth = (5/8)*H = 0.541266*Pitch

---
Threading - G76

---
Threading - G76

---
Threading - G76
G76 Pffppaa Qddd Rfff (first line of G76)‏
  - ff = # of finish passes (01-99)‏
  - pp = # revolutions for gradual pull-out (0.0-9.9=00-99)‏
  - aa = angle (60 degrees for us)‏
  - ddd = last depth of cut (min.cutting depth) (positive radial value, no decimal point – microns)‏
  - fff = finish allowance (mm, dec.point allowed)‏

---
Threading - G76
G76 Xxx Zzz Ppp Qqq Fff (2nd line)‏
  - xx = last thread pass diameter
  - zz = Z endpoint of thread
  - pp = height of thread (pos.radial value, microns)‏
  - qq = 1st threading pass depth (max.cutting depth, pos.radial value, microns)‏
  - ff = feedrate (same as thread lead)‏

---
Threading - G76
Example: M24x2 external thread
  - G00 X30.032 Z[#501 + 6.0]
  - G76 P010060 Q005 R0.0
  - G76 X24.43 Z[#501-10.0] P1360 Q0544 F2.0

---
Multistart Threading
Example: M24x2 three start external thread
  - #1=2.0 (PITCH - MM)‏
  - #2=0.5/TAN[30.0] * #1 (H)‏
  - #3=#2 * 17.0/24.0 (THREAD DEPTH)‏
  - #4=3 (NUMBER OF STARTS)‏
  - #5=0 (START NUMBER)‏
  - G00 X32.0 Z[#501 + 3 * #1 * #4] (START 3X LEAD AWAY)‏
  - WHILE [#5 LT #4] DO 1
  - G00 X30.032 Z[#501 + #1 * #5 + 3 * #1 * #4]
  - G76 P100060 Q005 R0.0
  - G76 X23.39 Z[#501-10.0] P[FIX[#3*1000]] Q0544 F[#1*#4]
  - #5 = #5 + 1
  - END 1