Stepper Motors

---
How Motors Run
https://www.youtube.com/watch?v=oP_EBgz8f_8

---
Electricity and Magnetism

---
Lorentz Force
https://en.wikipedia.org/wiki/Lorentz_force#Force_on_a_current-carrying_wire
F = qV x B
F ≈ i ∙ B (force per unit length)

---
Electricity and Magnetism

---
Step Motors
Full steps, 4 step/rev
http://www.pcbheaven.com/wikipages/How_Stepper_Motors_Work/
https://www.youtube.com/watch?v=lD_uAwZIjsI

---
Step Motors
2 Pole
Full steps, 4 step/rev
Half steps, 8 step/rev
Microstepping, 16 step/rev
http://www.pcbheaven.com/wikipages/How_Stepper_Motors_Work/

---
Step Motors
2 Pole
Full steps, 4 step/rev
Half steps, 8 step/rev
Microstepping, 16 step/rev
http://www.pcbheaven.com/wikipages/How_Stepper_Motors_Work/

---
Step Motor
6 pole

---
Step Motor
6 pole, 1 phase on

---
Step Motor
6 pole, 2 phase on

---
Typical Stepper Motor
N S

---
Selecting Step Motors
- Torque
- Speed
- Size, shaft diameter

---
Torque/Speed – NEMA 17 size
$20 motor

---
Torque/Speed – NEMA 34 size
$160 motor

---
Step Motor Drives

---
Step Motor Drives
https://www.pololu.com/product/1182

---
STEP/DIR signals
- each pulse to STEP moves motor one microstep
- DIR signal determines direction of movement

---
Types of Steppers
(OMC-Stepperonline.com)
NEMA6	14x14mm	0.6Ncm	$52
NEMA8	20x20mm	1.6Ncm	$16
NEMA11	28x28mm	7Ncm	$12

---
Types of Steppers
NEMA17	42x42mm	26Ncm	$8
Pancake NEMA11	28x28mm	1Ncm	$21
Hollow shaft NEMA14	35x35mm	18Ncm	$13

---
Types of Steppers
NEMA8 Geared 90:1	100Ncm	$45
NEMA11 Non-captive	2mm lead	$24
NEMA11 External	2mm lead	$28

---
Types of Steppers
NEMA11 Captive	0.635mm lead	$93

---
Motor Couplings
Beam or Helical Coupling	$1
Spider Coupling	$5

---
Motion Profiles
Velocity Step

---
Motion Profiles
Velocity Ramp (trapezoidal profile)
http://picprog.strongedge.net/step_prof/step-profile.html

---
Motion Profiles
Trapezoidal profile step pulses

---
Motion Profiles
Acceleration Ramp (jerk limited)

---
Accuracy

---
Grip and Rotate